## Slide 1: California State University, Los Angeles
“Enhanced Interior Gateway Routing Protocol”
Presented By Group#11:
Rajnish Kumar [304470392]
Manan Patel [304373828]
Gaurav Prajapati [304470132]
Guided By:
Edmund Gean
(Professor)

## Slide 2: Overview
About EIGRP
IGRP Vs. EIGRP
Advantages
Terminology
EIGRP Packets
Project Demo

## Slide 3: About EIGRP
Cisco proprietary protocol, advanced version of IGRP
Hybrid Routing protocol (best of SPF and Distance vector)
Supports CIDR/VLSM
Supports multiple routed protocols independently
EIGRP includes following features:
1. Reliable Transport Protocol (RTP)
2. Bounded Updates
3. Diffusing Update Algorithm (DUAL)
4. Establishing Adjacencies
5. Neighbor and Topology Table

## Slide 4: IGRP Vs. EIGRP
Similarities
  Both developed by Cisco
  Both calculate metrics using bandwidth and delay
  Use autonomous system numbers
Differences
  EIGRP scales metric of IGRP by a factor of 256 (EIGRP=32 bits, IGRP=24 bits)
  Hop count, IGRP=255, EIGRP=224
  EIGRP supports CIDR/VLSM
  EIGRP offers multi-protocol support
  => The main reason to replace IGRP to EIGRP is that the design of Internet Protocol had been changed to support classless IPV4 addresses.

## Slide 5: Advantages
Low usage of network resources during normal operation
When a change occurs, only routing table changes are propagated, not the entire routing table, this reduces the load the routing protocol itself places on the network
Rapid convergence times for changes in the network topology
EIGRP uses the Diffusing Update Algorithm (DUAL) to issue queries to neighbors for a loop-free route to the destination.

## Slide 6: Terminology
Term | Definition
Neighbor Table | Lists adjacent routers
Topology Table | Each router has one of each network protocol
Routing Table | Chooses routes from topology table – maintains one of each network protocol
Successor | Route selected as the primary route to use to reach a destination
Feasible Successor | A back up route

## Slide 7: EIGRP Packets
Hello
Acknowledgement
Update
Query
Reply

## Slide 8: EIGRP Packet Header

## Slide 9: Hello Packets

## Slide 10: Update and ACK Packets

## Slide 11: Query & Reply Packets

## Slide 12: Project Demo
Network Diagram
To Do:
EIGRP Configuration
Capturing and Decoding EIGRP Packets

## Slide 13: Configuration (Router1)
Router1> en
Router1# config t
Router1(config)# int fastEthernet 0/0
Router1(config-if)# ip address 12.12.12.2 255.255.255.0
Router1(config-if)# no shutdown
Router1(config-if)# exit
Router1(config)# int fastEthernet 1/0
Router1(config-if)# ip address 11.11.11.1 255.255.255.0
Router1(config-if)# no shutdown
Router1(config-if)# exit
Router1(config)# int fastEthernet 1/1
Router1(config-if)# ip address 2.2.2.1 255.255.255.0
Router1(config-if)# no shutdown
Router1(config-if)# exit
Router1(config)# router eigrp 10
Router1(config-router)# network 12.12.12.0
Router1(config-router)# network 11.11.11.0
Router1(config-router)# network 2.2.2.0
Router1(config-router)# exit
Router1(config)# exit
Router1#

## Slide 14: Configuration (Router2)
Router2> en
Router2# config t
Router2(config)# int fastEthernet 0/0
Router2(config-if)# ip address 10.10.10.2 255.255.255.0
Router2(config-if)# no shutdown
Router2(config-if)# exit
Router2(config)# int fastEthernet 1/0
Router2(config-if)# ip address 11.11.11.2 255.255.255.0
Router2(config-if)# no shutdown
Router2(config-if)# exit
Router2(config)# int fastEthernet 1/1
Router2(config-if)# ip address 3.3.3.1 255.255.255.0
Router2(config-if)# no shutdown
Router2(config-if)# exit
Router2(config)# router eigrp 10
Router2(config-router)# network 10.10.10.0
Router2(config-router)# network 11.11.11.0
Router2(config-router)# network 3.3.3.0
Router2(config-router)# exit
Router2(config)# exit
Router2#

## Slide 15: Configuration (Router3)
Router3> en
Router3# config t
Router3(config)# int fastEthernet 0/0
Router3(config-if)# ip address 10.10.10.1 255.255.255.0
Router3(config-if)# no shutdown
Router3(config-if)# exit
Router3(config)# int fastEthernet 1/0
Router3(config-if)# ip address 12.12.12.1 255.255.255.0
Router3(config-if)# no shutdown
Router3(config-if)# exit
Router3(config)# int fastEthernet 1/1
Router3(config-if)# ip address 1.1.1.1 255.255.255.0
Router3(config-if)# no shutdown
Router3(config-if)# exit
Router3(config)# router eigrp 10
Router3(config-router)# network 10.10.10.0
Router3(config-router)# network 12.12.12.0
Router3(config-router)# network 1.1.1.0
Router3(config-router)# exit
Router3(config)# exit
Router3#

## Slide 16: Configuration (PC)
PC1:
IP Address: 2.2.2.2
Subnet Mask: 255.255.255.0
Default Gateway: 2.2.2.1
PC2:
IP Address: 3.3.3.2
Subnet Mask: 255.255.255.0
Default Gateway: 3.3.3.1
PC3:
IP Address: 1.1.1.2
Subnet Mask: 255.255.255.0
Default Gateway: 1.1.1.1

## Slide 17: Neighbors Table (For All 3 Routers)

## Slide 18: Topology Table (Router1)

## Slide 19: Topology Table (Router2)

## Slide 20: Topology Table (Router3)

## Slide 21: Routing Table (Router1)

## Slide 22: Routing Table (Router2)

## Slide 23: Routing Table (Router3)

## Slide 24: EIGRP Packets: Hello & ACK

## Slide 25: EIGRP Packets: Reply, Query

## Slide 26: EIGRP Packets: Update

## Slide 27: Any Questions??..

## Slide 28: Thank you..